Digital Design 2
Dr. Mohammed Shalan
Project 1 Report: Logic Circuit Schematic Beautifier
Group: Mohammed R. Anany and Ahmed A. Agiza

Outline:
The application receives a netlist as input, parses it into components and wires, applies Sugiyama's algorithm on it, and produces a graphical representation of the circuit.

Technology Used:
- Node.js framework for the back-end.
- Express.js application framework.
- Joint.js graphing library.
- Alloy-UI for the front-end of the application.

Design and Implementation:

Models:
The implementation of the system depended on the existence of three main models:
- Components
- Parser
- GraphBuilder

The Component model is capable of holding information relating to gates and connections. It currently supports a good number of gates and is designed in such a way that extending it won't be difficult (maintainable). As for the wiring, it is capable of detecting whether it is an input port, an output port, or a connection between gates. The model also features a debugging facility which notifies the user of flying wires that may exist in the input netlist.

The Parser model is the one that takes an an input the netlist. It is capable of detecting many key elements in the file such as gates, wires, buses, parameters (with dot notation), and assign statements as well. After parsing the content, it returns with the parsed gates, wires, and any possible warnings that were detected. The following is a screen shot of the array of gates produced:

The GraphBuilder model is responsible for handling the positioning of the gates in the graph. It applies Sugiyama's algorithm which is broken down into a few steps. First, a directed graph is constructed, then the nodes are assigned into layers (Longest Path Layering). The graph is then properly layered by adding dummy nodes. The next step is to reduce the number of crossings between the edges (Barycenter Layer-by-Layer Sweep). Absolute values are then assigned to the gates' coordinates making it ready for plotting. The following is a screen shot showing the relative and absolute values for the coordinates of the gates:

Application Interface:
Upon opening the application the user is prompted to upload the desired netlist file. After uploading it.:

The user is then directed to another url where the interface is dividing into 3 main windows: The text editor, the console, and the circuit. The editor looks like the following:

The console looks like this:

After the GraphBuilder specifies the location of the elements in the graph the returned data is then taken as input to the module responsible for graphing it using Joint.js. The following is a screen shot of a circuit after it has gone through all the stages up to the graphing:

Testing Strategy:
For testing, we used an incremental approach. Each part was first tested alone. The parser was run separately from the rest of the application using multiple netlists that we wrote. The graphing library was tested using hard-coded data initially to see how the graphing elements will look. The sorting and placement algorithms were also testing initially with hard-coded graph data structures. Once each element was working separately, we combined the parser and the algorithms, then we check to see if the output is still correct. We then wired up the graphing library to the output of the algorithms stage. The User Interface was gradually introduced while the application was being developed.