Digital Design 2
Dr. Mohammed Shalan
Project 1: Logic Circuit Schematic Beautifier

Algorithmic Approach to a Layered Graph

Input: The input for this stage will be an array of Gate objects that will be used to construct a directed acyclic graph (DAG) representing the circuit that is to be generated.

Expected output: The output of this stage should be a layout for the graph that is to be drawn such that:
- The graph is organized in layers where all edges are going from top to bottom (or left to right).
- Edge crossing is minimized.
- The layers are not too wide.
- The height of the graph is reasonable.

The approach that I will be using is following the methodology of Sugiyama, which involves the following:
- Removing existing cycles by reversing the direction of some edges in the graph.
- Assigning vertices to layers using a heuristic approach.
- Introducing dummy vertices between 2 nodes that are not on 2 consecutive layers.
- Reducing the crossings among the edges by permuting the order of each layer.
- Remove the dummy nodes and replace them with edge bends.
- Reduce the number of bends by readjusting the position of vertices on each layer.

The hierarchical approach consists of 3-4 main steps:
- Layer assignment: each vertex is assigned a horizontal layer, its y-coordinate.
- Crossing reduction: the vertices within a layer are ordered to reduce edge crossings.
- Horizontal coordinate assignment: each vertex is assigned an x-coordinate such that we distribute the vertices uniformly and reduce the number of edge bends. If the graph has cycles an extra step is required:
- Cycle removal: As few edges as possible are reversed to achieve an acyclic graph. At the end of the algorithm the reversed edges are restored again to maintain the original orientation.

Most of these steps are NP-complete, and so a variety of heuristics will be used. For each of these main steps there are multiple ways to achieve the task. Listed below are the alternatives for each stage:

Cycle Removal (Not Needed: The input is going to be a DAG):
- Fast Heuristic.
- Enhanced Greedy Heuristic.

Layering Assignment:
- Longest path layering.
- Layering to minimize width (Coffman-Graham-Layering).
- Minimize number of dummy vertices.

Crossing Reduction (Layer-by-Layer Sweep is going to be applied for all):
- Sorting Method (Adjacent-Exchange / Split).
- Barycenter Method.
- Median Method.
- Integer Programming Method: Exact Algorithm.

Horizontal Coordinate Assignment
Depends on how the graph is going to be laid out.

The combination that I will implement to achieve the layout:
- For the layering assignment, I will use the Longest Path Layering which minimizes the height of the graph.
- For the Crossing Reduction, I will use an averaging method (Barycenter or Median) and use the Layer-by-Layer approach (in which we will solve the two-layer crossing problem for each pair of adjacent layers.
- The Horizontal Coordinate Assignment step is still to be determined.

The Longest Path Layering algorithm was chosen because it performs in a linear time complexity, however the graph tends to be very wide at the bottom.
For the Crossing reduction I chose an averaging method because this is the most commonly used approach to the problem and is shown to yield better results.
The horizontal coordinate assignment step depends on the layout of the graph (absolute references).